## Slide 1: CSE 4128 : Image Processing and Computer Vision Laboratory
Osteosarcoma Cell Nucleus Segmentation
Presented By:
Ahsanul Haque Hasib
Roll: 2007020
Department of Computer Science and Engineering
Khulna University of Engineering & Technology
Supervised by:
Dr. Sk. Md. Masudul Ahsan
Professor Department of Computer Science and Engineering Khulna University of Engineering & Technology Md Tajmilur Rahman
Lecturer Department of Computer Science and Engineering Khulna University of Engineering & Technology

## Slide 2
Objectives
Introduction
Tools Used
Methodology
User Interface
Limitations
Conclusion
References
Outline

## Slide 3
To develop an automated system to detect and segment Osteosarcoma cell nuclei.
To utilize image processing algorithms for the implementation of the whole system.
To try and ensure high accuracy in identifying the nucleuses.
To get an approximate count of the nucleuses along with individual descriptors for each segmented object.
To create a user-friendly interface for uploading, processing and displaying the segmented image along with intermediate results with step‑by‑step visualization and parameter control (σ, method variants).
Objectives

## Slide 4
Osteosarcoma is a highly malignant primary bone tumor that predominantly affects children and young adults.
Localized histogram equalization with clipping control, improved nuclear visibility without amplifying noise.
Smoothing reduces random noises and fluctuations.
Thresholding separates nuclei from background automatically by maximizing between-class variance in gray-level distribution.
Morphological operations and connected component labeling finally derives the segmented result.
These classical methods are transparent, computationally efficient, and well-suited for histopathological image analysis and cytology.
Introduction

## Slide 5
Python
OpenCV (Open Source Computer Vision Library)
Numpy
Gradio (For designing User Interface)
Tools Used

## Slide 6
Methodology
Figure-1: Flow Diagram for the whole system
  Blue Channel extraction from DAPI-stained image.
  Perform Histogram Equalization(Global and CLAHE).
  Denoise using Gaussian filter.
  Threshold the smoothed image using Otsu’s Thresholding.
  Morphological operations like opening and closing for removing salt noise and filling holes.
  Labelling each segments using connected components.
  Extract boundary for each segments and get descriptors.
  Display the final segmented output with boundaries overlayed and total counts.
Source: Adapted from Win, K. Y. et al.(2018). Comparative Study on Automated Cell Nuclei Segmentation Methods for Cytology Pleural Effusion Images.

## Slide 7
Blue channel extraction
So the blue channel must be extracted prior-hand.
Methodology(Contd.)
Pre-processing
Figure-2: (a)Osteosarcoma Nuclei highlighted with DAPI stain (b) Blue channel extracted
Source: microscopyu.com/
(a)
(b)

## Slide 8
Contrast Enhancement
  So it while .
Methodology(Contd.)
Pre-processing
Figure-3: Flow Diagram of CLAHE
Source: J. Lee et al. (2015). An Adaptive Histogram Equalization Based Local Technique for Contrast Preserving Image Enhancement.

## Slide 9
Let L = 256 gray levels. Given a tile T of size (tₕ × tw):
  Compute histogram h[0 … L−1] and total pixel count |T|.
  Compute per-bin clip threshold: hₘₐₓ = clip_limit × (|T| / L)
  Clip the histogram: h̃[i] = min(h[i], hₘₐₓ) Accumulate the excess: E = Σ (h[i] − hₘₐₓ),
  Redistribute excess uniformly: ĥ[i] = h̃[i] + (E / L)
  Normalize to a PDF: p[i] = ĥ[i] / Σĥ[j] Compute cumulative distribution: c[i] = Σₖ₌₀ⁱ p[k]
  Build lookup table: sk[i] = ⌊c[i] × (L−1)⌋
  Remap tile T using the lookup table.
Methodology(Contd.)
Pre-processing(Contrast Enhancement)
Figure-4: (a) Blue channel image
(b) Histogram Equalized image
(a)
(b)

## Slide 10
Smoothing
    Gσ(x, y) = · e−
Methodology(Contd.)
Pre-processing
Figure-5: (a) Histogram Equalized image
(b) Smoothed image
(a)
(b)

## Slide 11
Smoothing
  .
  Between-class variance: σB 2 =
The Otsu threshold k⁎ is the gray level that maximizes σB².
Methodology(Contd.)
Segmentation (Otsu’s Thresholding)
(a)
(b)
Figure-6: (a) Smoothed image
(b) Otsu’s Thresholded image

## Slide 12
Algorithm:
  Compute normalized histogram pᵢ for i = 0, …, L−1.
  Compute cumulative sums P₁(k) for k = 0, …, L−1.
  Compute means m(k) for k = 0, …, L−1.
  Compute the global mean mG.
  For each k, compute σB²(k) and track the maximum value.
  Set k* = k that gives the maximum between-class variance.
Methodology(Contd.)
Segmentation(Otsu’s Thresholding)

## Slide 13
Morphological Operations
  : An erosion followed by dilation.
        Ib ∘ B = (Ib ⊖ B) ⊕ B
  Here Ib is the thresholded image and B is the structuring element of 1’s in 3x3.
  Using Opening we can remove some high frequency noise that retained even after thresholding.
Methodology(Contd.)
Post-processing
Figure-7: (a) Before Opening (b) after Opening with small background noise removed.
(b)
(a)

## Slide 14
Morphological Operations
  : A dilation followed by erosion.
        Ib ∙ B = (Ib ⊕ B) ⊖ B
  Here Ib is the resultant image after opening and B is the structuring element of 1’s in 3x3.
  Using Closing we can remove small black holes within the object.
Methodology(Contd.)
Post-processing
Figure-8: (a) Before Closing (b) after Closing with small foreground hole filled.
(b)

## Slide 15
Boundary extraction
  For this we perform erosion then subtract the eroded image from thresholded image to get boundary.
        Boundary = Ib - (Ib ⊖ B)
  Here Ib is the resultant image after closing and B is the structuring element of 1’s in 3x3.
Methodology(Contd.)
Post-processing
Figure-9: (a) After Closing (b) Boundary extracted
(b)

## Slide 16
Cell counting and labeling
  For this we used DFS traversal in the segmented image and labeled the pixels of same connected neighborhood with the same label.
Algorithm
Initialize label matrix L(x, y) with zeros.
For each pixel (x, y): • If M₂(x, y) = 1 (foreground) and L(x, y) = 0, assign a new label k. • Push (x, y) to a stack for region growing.
While the stack is not empty: • Pop a pixel (x′, y′). • For each of its 8-connected neighbors (xₙ, yₙ): – If M₂(xₙ, yₙ) = 1 and L(xₙ, yₙ) = 0, assign label k and push it to the stack.
Increment k and repeat until all pixels are visited.
The total nucleus count is N = k − 1.
Methodology(Contd.)
Post-processing

## Slide 17
Region Descriptors
  For each cell we compute the following:
Compute region geometry: • Area: Aₖ = number of foreground pixels in each object • Perimeter: Pₖ = number of boundary pixels of object. • Maximum diameter: Dₖ = maximum distance between any two pixels in object.
Compute shape descriptors: • Compactness: Cₖ = (Pₖ²) / Aₖ • Form factor: Fₖ = (4πAₖ) / (Pₖ²) • Roundness: Rₖ = (4Aₖ) / (πDₖ²)
Methodology(Contd.)
Post-processing

## Slide 18
User Interface
Figure-10: User Interface

## Slide 19
User Interface(Contd.)
Figure-11: (a) Original Image (b) Blue Channel Extracted

## Slide 20
User Interface(Contd.)
Figure-12: (a) Blue Channel Extracted (b) Histogram Equalized Image(CLAHE)

## Slide 21
User Interface(Contd.)
Figure-13: (a) Histogram Equalized Image(CLAHE) (b) Gaussian blurred Image

## Slide 22
User Interface(Contd.)
Figure-14: (a) Gaussian blurred Image (b) Otsu Thresholded Image

## Slide 23
User Interface(Contd.)
Figure-15: (a) Otsu Thresholded Image (b) Opening

## Slide 24
User Interface(Contd.)
Figure-16: (a) Opening (b) Closing

## Slide 25
User Interface(Contd.)
Figure-17: (a) Closing (b) Boundaries extracted

## Slide 26
User Interface(Contd.)
Video-1: Demonstration

## Slide 27
User Interface(Contd.)

## Slide 28
Otsu assumes bimodality; very uneven illumination or non-bimodality reduces it's efficiency.
CLAHE parameters are image-dependent; excessive clipping can wash out contrast, too little reverts toward AHE and can amplify noise.
Current morphological and threshold-based pipelines cannot fully separate overlapping or touching nuclei, which remain a major limitation.
Limitations

## Slide 29
This work presents an end-to-end, interpretable, and modular pipeline for osteosarcoma nuclei segmentation using purely classical image processing method.
Despite its simplicity, the system exhibits limitations due to global thresholding and morphological segmentation; including inability to resolve overlapping nuclei.
Conclusion

## Slide 30
K. Zuiderveld. (1994), “Contrast Limited Adaptive Histogram Equalization (CLAHE)”.
J. Lee et al. (2015), “An Adaptive Histogram Equalization Based Local Technique for Contrast Preserving Image Enhancement”.
K. Y. Win et al. (2018), “Comparative study on automated cell nuclei segmentation methods for cytology pleural effusion images”.
References

## Slide 31
THANK YOU!